## Slide 1: TU856-1 & TU858-1 Computer Architecture and Technology Module Code: CMPU 1006
COMPUTING AND ITS HISTORY – an Overview
Presenter: Dr Art Sloan
Semester 1, Week 1

## Slide 2: Presentation Outline
This presentation is a rapid journey through the development of computers – from small mechanical calculators to multi-core processors.
It will focus on the functional structures of the examples given – an architectural perspective.
There is ‘diversion’ in the mid section of the presentation to give the background of the people and society in which electronic computers developed most rapidly.

## Slide 3: Presentation Content - including
Computer System
Hardware of the Computer System
Software of the Computer System
Before Babbage (Schickard – Leibniz)
Charles Babbage
Herman Hollerith
ENIAC, EDVAC, EDSAC
Transistors
Integrated Circuits
Microprocessors
Multicore Processors
Introduction to Computer Architecture
Lecture Summary
Where to Next?

## Slide 4: Computer…?
A computer is a device – usually an electronic device – that accepts information in the form of data and manipulates them for some result which is often output.
The manipulation is a process or method based on a computer program or sequence of instructions on how the data are to be processed.

## Slide 5: Computer!
Many computers also include the means for storing data and programs for a necessary period of time. Time that could be a nanosecond or a millennium.

## Slide 6: Computer System
What is a ‘system’?
A system is a generally defining word that implies that there exists a type of input, a type of procedure and a type of output.

## Slide 7: Computer System (2)
A computer system can be described as having
  input(s),
  procedure(s) or process(es),
  output(s).

## Slide 8: Computer System (3)
INPUT ---- PROCESS --- OUTPUT
A computer system is a set of hardware and software that processes data.
A relatively simple computer system is a personal computer.
An example of a complex computer system is the Internet.

## Slide 9: Computer System (4)
What makes a computer system even more useful is its ability to STORE data (or signals of a non-data type) after they have been output – or while data are output.
That output or stored data can be used as input in a ‘feedback loop’, if necessary.

## Slide 10: Computer System (5)
A computer system is a system because the two aspects of hardware and software have to work together.
A typical ‘computer system’ comes with interconnection capability. (Many computer systems can interconnect - that is, join to become a bigger system.)

## Slide 11: Hardware of a Computer System
‘Hardware’ is the term that encapsulates the electronic devices and circuitry that make up the physical components of the computer system.
These elements are the computer parts that you can see and touch.

## Slide 12: Hardware of a Computer System (2)
Examples of physical elements – (Hardware):
  Central Processing Unit (CPU),
  Primary storage,
  Secondary storage,
  Input devices,
  Output devices and
  Communications devices

## Slide 13: Software of a Computer System
‘Software’ is the term that describes the instructions (and data) that determine the use of the processing capability.
Software is often the invisible means of process that goes on as the computer is running.

## Slide 14: Software of a Computer System (2)
Examples of non-physical elements – (Software):
  Systems software and/or Operating Systems (O/S),
  Applications software,
  Database Management Systems (DBMS). (Optional for most computer systems.)
  Communications software (when connected to a network).

## Slide 15: System of Two Things
The two terms, hardware and software together encapsulate a working computer system.
This basic system allows a datum (singular) and data (a collection of datum) to be represented for input, processing and/or output.

## Slide 16: System of Two Things (2)
The physical elements are utilised by non-physical elements of instruction and coordination.

## Slide 17: History of Hardware
Next, let us go back to early devices for calculation, moving through time to very large-scale integrated circuits.
There is a diversion to mention von Neumann architecture (Systems Architecture) midway.

## Slide 18: Babbage and Before
There were simple, mechanical devices for calculating numbers – even dated around 1624.
Wilhelm Schickard lived from 1592 to 1635 was a Christian minister and a Professor of Hebrew, Eastern Languages, Astronomy and Mathematics, among other things, in Tubingen, Germany.

## Slide 19: Schickard’s Calculator
Wilhelm Schickard built this adding machine based on his mathematical ideas:
Front
Back

## Slide 20: Pascal’s Calculator
Blaise Pascal, the French mathematician, who lived from 1623 to 1662, had an adding and subtracting machine – built around 1642:
Pascal’s Arithmetic Machine

## Slide 21: Leibniz’s Calculator
Gottfried Wilhelm von Leibniz lived from 1646 to 1716 and is described as a lawyer, mathematician and a scientist of various other disciplines. His calculator appeared around 1671.
It was another apparatus of cogs and wheels…

## Slide 22: Leibniz’s Calculator (2)
… but it is said to be better than Pascal’s device since it could add, subtract, multiply and divide.
Leibniz’s Calculating Machine

## Slide 23: Charles Babbage
Charles Babbage was an English mathematician – but is often seen more of an inventor. He lived from 1791 to 1871.
His mechanical calculator was called the Difference Engine and is said to have been functional in 1822.
The machine was able to generate successive values of algebraic functions by means of finite differences.

## Slide 24: Charles Babbage (2)
The device seems to have worked like a series of Leibniz machines connected together – that is how it seems to me, anyway.
Babbage’s Difference Engine
Babbage for scale

## Slide 25: Charles Babbage (3)
After the Difference Engine Babbage set about the Analytical Engine. He did not complete this endeavour, having died, but the idea was to use Jaquard’s Loom (see Tutorial) technology to manipulate numbers;
Store numbers with a memory consisting of sets of counter wheels
A ‘mill’ as a kind of Arithmetic Logic Unit: a four-function arithmetic unit operating on variables stored on counter wheels and storing the result on a counter wheel
Printer or card punch to output the result
Operation cards to directed the operation to be performed
Variable Cards to call in the variables from the store

## Slide 26: Charles Babbage (4)
What is this? Some Web sites say it is the Analytical Engine in complete form. Historically, it was never properly built… but this may be a fair representation:
Babbage’s Analytical Engine?
For scale

## Slide 27: Charles Babbage (5)
The Mill
(Arithmetic
Functions)
The Store
(Memory)
Printer and
Punch Cards
Operation
Cards
Variable
Cards

## Slide 28: Hollerith’s Punched Cards
Herman Hollerith (1860 – 1929) designed a ‘tabulating machine’ based on punched cards – specifically for the 1890 United States census.
His breakthrough was his use of electricity to read, count, and sort punched cards whose holes represented data gathered by the census-takers.
His machines accomplished in one year what would have taken nearly ten years of tabulating by clerks. (Note; some sources suggest 2000 clerks employed, taking 6 weeks on the machine for the census (?).)

## Slide 29: Hollerith’s Machine
In 1896 Hollerith founded the Tabulating Machine Company (TMC) to sell his invention. The company developed into International Business Machines (IBM) in the 1920s.
Hollerith’s 1890 Census Machine

## Slide 30: Early 20th Century Computers
There were variations on mechanical and electro-mechanical computing devices. Transitory inventions. Consider:
Charles and Howard Krum’s Teleprinter
Vannevar Bush’s Differential Analyser
George Stibitz's Complex Number Calculator
Alan Turing’s (big contribution to Bletchley Park’s) Collossus

## Slide 31: Electronic Numerical Integrator And Computer (ENIAC)
Ballistics Research Laboratory, started 1935, Maryland USA to scientifically support the military. Keeping tables on weapons’ firing tests was difficult. 3,000 trajectories for a typical table took 100 people one month.
200 people were employed with calculators.
Along comes World War 2, along comes government investment, along comes ENIAC from the University of Pennsylvania.

## Slide 32: ENIAC (2)
ENIAC – (Electronic Numerical Integrator And Computer) is really the world's first electronic digital computer.

## Slide 33: ENIAC (3)
ENIAC was developed by Dr. J. Presper Eckert and Dr. John W. Mauchly.
It filled an entire room, weighed thirty tons, and consumed two hundred kilowatts of power.
More than 19,000 vacuum tubes were the principal elements in the computer's circuitry. It also had fifteen hundred relays and hundreds of thousands of resistors, capacitors, and inductors.

## Slide 34: EDVAC
EDVAC (Electronic Discrete Variable Automatic Computer) was Mauchly and Eckert’s next project – they started working on it two years before ENIAC even went into operation.
The program for the computer stored inside the computer, made possible by having more internal memory than any other computing device.
Memory used mercury delay lines. The idea being that given a tube of mercury, an electronic pulse could be bounced back and forth to be retrieved at will. Another two state device for storing 0s and 1s. This on/off switchability for memory was required because EDVAC used binary rather than decimal numbers, thus simplifying the construction of the arithmetic units.

## Slide 35: … a Small Diversion…
We need to divert from hardware history at this point, as Mauchly, Eckert and von Neumann developed a new idea on how vacuum tube-based hardware could handle instructions and data. (Around the mid-1940s)
This was a new architectural approach to systems.
Briefly, Systems Architecture History…

## Slide 36: John Von Neumann
John Von Neumann wrote a paper called ‘The First Draft’ which described the stored program concept.
He was involved with the ENIAC and the EDVAC projects.
He became associated with ‘inventing’ modern programming in a kind of scientific community mistake. (The concept was really Eckert and Mauchly’s.)

## Slide 37: EDVAC Layout
Main
Memory
Arithmetic
Logic Unit
Program
Control Unit
I/O
Equipment

## Slide 38: EDSAC
Meanwhile… over in England… a machine called the Electronic Delay Storage Automatic Calculator (EDSAC) started running at Cambridge University on 6th May 1949. It was a project by Professor Maurice Wilkes.
EDSAC contained 3,000 vacuum tubes and used mercury delay lines for memory.
Programs were input using paper tape and output results appeared on a teleprinter.
EDSAC is credited as using one of the first assemblers (more on assemblers in another lecture) called "Initial Orders," so it could be programmed symbolically rather than using machine code.

## Slide 39: EDSAC Specification
EDSAC had 512 words of 35 bits each of main RAM (Random Access Memory). (Total: just over 2 kilobytes.)
The RAM was made of 32 long tanks of mercury carrying ultrasonic sound pulses.
The system ran at a clock speed of 500kHz, but since the EDSAC was a serial computer, and because of the memory design, it managed about 600 instructions per second.
18 different instructions possible, each took 17 bits, or one half-word. Values could either be integers or fixed-point numbers (from -1 to 1), occupying either a whole 35-bit word or a 17-bit half-word.
The accumulator had a capacity of 71 bits.

## Slide 40: 1935 – 1950 Summary

## Slide 41: Back to Hardware History
Now we can go back to historic hardware – to pick up on the move away from vacuum tube technology and towards the alternatives that reduce the size of circuits and improve power efficiency…

## Slide 42: Transistors
Transistors are credited to John Bardeen, William Shockley, and Walter Brattain, scientists at the Bell Telephone Laboratories in New Jersey, U.S.A.
In the early 1950s they were researching the possibility of using crystals as semi-conductors - attempting to replace vacuum tubes as relays in telecommunications systems.
A very early Shockley, Bardeen, Brattain Transistor

## Slide 43: Transistors (2)
The transistor is a device composed of semi-conductor material that can both conduct and insulate. (Germanium and silicon can do that.)
Transistors switch and modulate electronic current.
The "point-contact" transistor amplifier.
-n emitter
p base
+n collector
Low voltage at base and emitter – higher voltage at collector and emitter

## Slide 44: Integrated Circuits
From 1956 transistors revolutionised computer hardware. The research, at that time, was to reduce the wiring and soldered connections.
Jack St. Clair Kilby, an engineer with Texas Instruments, manufactured the first integrated circuit or ‘chip’ in 1958. Robert Noyce, research engineer and co-founder the Fairchild Semiconductor Corporation was also making progress on a chip.
With transistor-type circuits the transistors, resistors, capacitors and all the connecting wiring are separate. The monolithic - or single crystal - integrated circuit placed all components and most wiring onto a single, semiconducting crystal.
Kilby used germanium and Noyce used silicon as the basis of their respective chips.

## Slide 45: Integrated Circuits (2)
Kilby and Noyce patented their devices separately but came to an agreement a few years after legal wrangling to allow both patents to act as one… Ker-ching!
The Kilby Integrated Circuit
The Noyce Integrated Circuit

## Slide 46: Microprocessors
1968, Bob Noyce (again) and Gordon Moore left ‘Fairchild’ and set up Intel. November 1971, Intel announced the world's first single chip microprocessor; the Intel 4004.
The 4004 was invented by Federico Faggin, Ted Hoff, and Stan Mazor, engineers at Intel.
This was more that just an integrated circuit - the Intel 4004 chip reduced the size requirements for a processor by placing the central processing unit, memory, input and output controls on one small chip.

## Slide 47: Microprocessors (2)
Layout for the Intel 4004

## Slide 48: Multi Core Processors
Place two or more processor circuits on one IC (integrated circuit) - or two or more individual processors to work together - and you have a ‘multicore’ (or multi-core) architecture. A core is a collection of one or more processor threads with the components to execute instructions – such as Arithmetic Logic Unit, Cache, RAM…
(N.B. Multi core arrangements usually contain much more cache than regular processors.)

## Slide 49: Multi Core Processors (2)
A thread (thread of execution) is ‘placeholder information’ associated with a single use of a program that can handle multiple concurrent users. A thread is like a task but is not actually an instruction task. Many ordinary, single-core processors can perform ‘multithreading’ - multiple threads are executed in parallel by ‘time slicing’ the processing capability of the processor and the processor can function by switching between different threads.

## Slide 50: Multi Core Processors (3)
Multiple terms for multi-core:
  ‘Multi-core’ – more than one core
  ‘Dual-core’ – two CPU cores on one IC or two separate ICs
  ‘Multi-chip module’ – an alternative name for two or more separate ICs
  ‘Double core’ or ‘twin core’ - alternative names for two separate ICs
  ‘Quad-core’ – four CPU cores on one IC or two separate ICs

## Slide 51: Multi Core Processors (4)
Microsoft’s multi-core diagrams:
3
1
2

## Slide 52: Multi Core Processors (5)
Dual core block diagram:

## Slide 53: Multi Core Processors - Summary
A dual core set-up is comparable to having multiple, separate processors installed in the same computer, but because the two processors are actually plugged into the same socket, the connection between them is faster. Ideally, a dual core processor is nearly twice as powerful as a single core processor. In practice, performance gains are about fifty percent: a dual core processor is about one-and-a-half times as powerful as a single core processor.

## Slide 54: Back to Architecture, Briefly
We can go back to architecture to finish the lecture.
This is just to introduce the principle of computer architecture…

## Slide 55: Introducing Architecture
Computer architecture can be a reference model, such as the Open Systems Interconnection (OSI) reference model, intended as a model for specific product architectures, or it can be a specific product architecture, such as that for an Intel microprocessor or for one of IBM's or Microsoft’s operating systems.

## Slide 56: Introducing Architecture (2)
Architecture can be divided into five fundamental components:
  input/output,
  storage,
  communication,
  control,
  processing.
In practice, each of these components (sometimes called subsystems) is sometimes said to have an architecture of its own.

## Slide 57: Introducing Architecture (3)
By comparison, the term design might be considered as having less scope than architecture.
An architecture is a design, but most designs are not architectures. A single component or a new function has a design that has to fit within the overall architecture.
In hardware terms, the architecture is a very detailed description of every component – even the microscopic ones of the processor(s) – and their interaction.

## Slide 58: End of Historic Overview
That describes the module content and some of the features and events of computer (architecture) history.
Are there…
ANY QUESTIONS?

## Slide 59: Where to Next?
NEXT TIME (Monday 10 February):
The theme of the next lecture:
“Computers and Electricity”
How do computers work physically? How is computer architecture electronic? What is so special about electricity, where computer hardware is concerned? We can look at these things next.

## Slide 60
Thanks for your attentiveness.
See you here next time. Be safe and well in the meantime.