## Slide 1: TU856-1 and TU858-1 Computer Architecture and Technology
(Week 4) Tutorial 2
Thursday 20 February 2025

## Slide 2: Questions and Answers ( 1 )
How can we consider the use of binary to represent all instructions and data on a computer system?
The two-state number system can be compared with ‘relay’ components and ‘switching’ – which makes up hardware architecture at its most fundamental levels.

## Slide 3: Questions and Answers ( 2 )
A discursive investigation of Two’s Complement and how that works mathematically (as a method for subtraction and division).
Two’s Complement number conversion: 110
I.E. how do you find the decimal -1 in 8-bit binary?
0000 00012 (This is decimal 1 in 8-bit binary)
Flip 1s to 0s and 0s to 1s to get One’s Complement
1111 1110
Add a binary 1 to this to get Two’s Complement
1111 1111 (This can represent -12)

## Slide 4: Two’s Complement again
Two’s Complement numbers can be used in calculations by the computer to have the effect of subtraction.
A few more examples on the right

## Slide 5: Questions and Answers ( 3 )
What use has octal as a number base?
The use of three-place number systems.
Example
Older mainframe computers from 1950 and early 1960s used 12-bit, 24-bit or 36-bit words. Divisible by 3, so 3-bit octal labels fitted them for calculations.

## Slide 6: Questions and Answers ( 4 )
What use has hexadecimal as a number base?
The use of four-place number systems.
Example
Computers from 1960s onward use 16-bit, 32-bit or 64-bit words. Divisible by 4, so 4-bit hexadecimal labels fit them for calculations.

## Slide 7: Typical Exam (Sub) Question For This Content
Question
Give a brief description of binary, octal and hexadecimal number representations.
Sample solution
Binary
  Computing machines operate on electrical current and so use two states. We view these states as the numbers 0 and 1.
  This is the binary representation and is called 'Base 2'.
  Whether in decimal or binary, the position of numbers delineate their quantity.

## Slide 8: Solution continued
Octal
  Grouping binary digits, for example, 010010101110011 into threes looks like this:
9,58710 = |010|010|101|110|0112
  The Octal notation for representing Binary numbers uses groups of three bits:
  The symbols that are used to represent each group are the same as the integer value of each group. By using these Octal symbols (0 - 7), the number can be expressed in a more compact form:
9,58710 = (2|2|5|6|3) 8

## Slide 9: Solution continued
Hexadecimal
  Suppose that we group the example binary digits 010010101110011 into fours. Then this might be written:
9,58710 = |0010|0101|0111|00112
  Now the groups of four can be given different symbols.
  There are 16 different combinations of four binary digits.
  The symbols chosen are the common numerals (0 - 9) and the remaining six possible four-bit combinations are represented by the letters, A, B, C, D, E and F.
(10 marks)